# SECTION 1: IDENTIFICATION

# 1.1.       Product Identifier

Product Form: Substance

Product Name: Sodium Borate

CAS-No.: 1303-96-4

Formula: Na2B4O7 10H20

# 1.2.       Intended Use of the Product  No additional information available

# 1.3.       Name, Address, and Telephone of the Responsible Party

| Manufacturer Quality Science Labs, LLC P.O. Box 159, 37888 Highway 24 Lake George, CO 80827 Tel: 866.700.1884 www.qualitysciencelabs.com |  |
| --- | --- |

# 1.4.       Emergency Telephone Number

| Emergency Number | : | CHEMTREC 24 Hour Emergency: Phone Number (800) 424-9300 |
| --- | --- | --- |

SECTION 2: HAZARDS IDENTIFICATION

# 2.1.       Classification of the Substance or Mixture

| Eye Irrit. 2 | H319 |
| --- | --- |
| Repr. 1B | H360 |
| Aquatic Acute 3 | H402 |

Full text of hazard classes and H-statements : see section 16

# 2.2.       Label Elements

# GHS-US Labeling

| Hazard Pictograms (GHS-US) | : | GHS07 | GHS08 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Signal Word (GHS-US) | : | Danger |
| Hazard Statements (GHS-US) | : | H319 - Causes serious eye irritation. H360 - May damage fertility or the unborn child. H402 - Harmful to aquatic life. |
| Precautionary Statements (GHS-US) | : | P201 - Obtain special instructions before use. P202 - Do not handle until all safety precautions have been read and understood. P264 - Wash hands, forearms, and other exposed areas thoroughly after handling. P273 - Avoid release to the environment. P280 - Wear protective gloves, protective clothing, and eye protection. P305+P351+P338 - If in eyes: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P308+P313 - If exposed or concerned: Get medical advice/attention. P337+P313 - If eye irritation persists: Get medical advice/attention. P405 - Store locked up. P501 - Dispose of contents/container in accordance with local, regional, national, and international regulations. |

# 2.3.       Other Hazards

Exposure may aggravate pre-existing eye, skin, or respiratory conditions.

# 2.4.       Unknown Acute Toxicity (GHS-US)

No data available

SECTION 3: COMPOSITION/INFORMATION ON INGREDIENTS

# 3.1.       Substance

| Name | : | Sodium Borate |
| --- | --- | --- |
| CAS-No. | : | 1303-96-4 |
| Name | Synonyms | Product Identifier | % | GHS US classification |
| Borax (B4Na2O7.10H2O) | Borax / Borax (Na2(B4O7).10H2O) / Sodium tetraborate decahydrate / Disodium tetraborate, decahydrate / Sodium tetraborate, decahydrate / Disodium tetraborate decahydrate / Sodium borate decahydrate / Sodium borate, decahydrate / SODIUM BORATE DECAHYDRATE / Sodium borate / Borax decahydrate / Disodium tetraborate, anhydrous | (CAS-No.) 1303-96-4 | 100 | Eye Irrit. 2A, H319 Repr. 1B, H360 Aquatic Acute 3, H402 |

Full text of H-phrases: see section 16

# 3.2.       Mixture

Not applicable

# SECTION 4: FIRST AID MEASURES

# 4.1.       Description of First-aid Measures

First-aid Measures General: Never give anything by mouth to an unconscious person. If you feel unwell, seek medical advice (show the label where possible).

First-aid Measures After Inhalation: When symptoms occur: go into open air and ventilate suspected area. Obtain medical attention if breathing difficulty persists.

First-aid Measures After Skin Contact: Immediately drench affected area with water for at least 15 minutes. Remove contaminated clothing. If exposed or concerned: Get medical advice/attention.

First-aid Measures After Eye Contact: Immediately rinse with water for at least 15 minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Obtain medical attention if irritation develops or persists.

First-aid Measures After Ingestion: Rinse mouth. Do NOT induce vomiting. Obtain medical attention.

# 4.2.       Most Important Symptoms and Effects Both Acute and Delayed

Symptoms/Injuries: Causes serious eye irritation. May damage fertility. May damage the unborn child.

Symptoms/Injuries After Inhalation: Prolonged exposure may cause irritation.

Symptoms/Injuries After Skin Contact: Prolonged exposure may cause skin irritation.

Symptoms/Injuries After Eye Contact: Contact causes severe irritation with redness and swelling of the conjunctiva.

Symptoms/Injuries After Ingestion: Ingestion may cause adverse effects.

Chronic Symptoms: May damage fertility or the unborn child.

# 4.3.       Indication of Any Immediate Medical Attention and Special Treatment Needed

If exposed or concerned, get medical advice and attention. If medical advice is needed, have product container or label at hand.

# SECTION 5: FIRE-FIGHTING MEASURES

# 5.1.       Extinguishing Media

Suitable Extinguishing Media: Water spray, fog, carbon dioxide (CO2), alcohol-resistant foam, or dry chemical.

Unsuitable Extinguishing Media: Do not use a heavy water stream. Use of heavy stream of water may spread fire.

# 5.2.       Special Hazards Arising From the Substance or Mixture

Fire Hazard: Not considered flammable but may burn at high temperatures.

Explosion Hazard: Product is not explosive.

Reactivity: Hazardous reactions will not occur under normal conditions.

# 5.3.       Advice for Firefighters

Precautionary Measures Fire: Exercise caution when fighting any chemical fire.

Firefighting Instructions: Use water spray or fog for cooling exposed containers.

Protection During Firefighting: Do not enter fire area without proper protective equipment, including respiratory protection.

Hazardous Combustion Products: Sodium oxides. Borane/boron oxides.

Other Information: Do not allow run-off from fire fighting to enter drains or water courses.

# SECTION 6: ACCIDENTAL RELEASE MEASURES

# 6.1.       Personal Precautions, Protective Equipment and Emergency Procedures

General Measures: Do not get in eyes, on skin, or on clothing. Do not breathe dust.

# 6.1.1.      For Non-Emergency Personnel

Protective Equipment: Use appropriate personal protective equipment (PPE).

Emergency Procedures: Evacuate unnecessary personnel.

6.1.2.      For Emergency Personnel

Protective Equipment: Equip cleanup crew with proper protection.

Emergency Procedures: Upon arrival at the scene, a first responder is expected to recognize the presence of dangerous goods, protect oneself and the public, secure the area, and call for the assistance of trained personnel as soon as conditions permit. Ventilate area.

# 6.2.       Environmental Precautions

Prevent entry to sewers and public waters. Avoid release to the environment.

# 6.3.       Methods and Materials for Containment and Cleaning Up

For Containment: Contain solid spills with appropriate barriers and prevent migration and entry into sewers or streams.

Methods for Cleaning Up: Recover the product by vacuuming, shoveling or sweeping. Transfer spilled material to a suitable container for disposal. Clean up spills immediately and dispose of waste safely. Contact competent authorities after a spill.

# 6.4.       Reference to Other Sections

See Section 8 for exposure controls and personal protection and Section 13 for disposal considerations.

# SECTION 7: HANDLING AND STORAGE

# 7.1.       Precautions for Safe Handling

Precautions for Safe Handling: Avoid contact with skin, eyes and clothing. Wash hands and other exposed areas with mild soap and water before eating, drinking or smoking and when leaving work. Obtain special instructions before use. Do not handle until all safety precautions have been read and understood. Do not breathe dust.

Hygiene Measures: Handle in accordance with good industrial hygiene and safety procedures.

# 7.2.       Conditions for Safe Storage, Including Any Incompatibilities

Technical Measures: Comply with applicable regulations.

Storage Conditions: Keep container closed when not in use. Store in a dry, cool place. Keep/Store away from direct sunlight, extremely high or low temperatures and incompatible materials. Store locked up/in a secure area.

Incompatible Materials: Strong acids, strong bases, strong oxidizers.

7.3.       Specific End Use(s)  No additional information available

# SECTION 8: EXPOSURE CONTROLS/PERSONAL PROTECTION

# 8.1.       Control Parameters

For substances listed in section 3 that are not listed here, there are no established exposure limits from the manufacturer, supplier, importer, or the appropriate advisory agency including: ACGIH (TLV), AIHA (WEEL), NIOSH (REL), or OSHA (PEL).

| Borax (B4Na2O7.10H2O) (1303-96-4) |
| --- |
| USA ACGIH | ACGIH TWA (mg/m³) | 2 mg/m³ (inhalable particulate matter (Borate compounds, inorganic) |
| USA ACGIH | ACGIH STEL (mg/m³) | 6 mg/m³ (inhalable particulate matter (Borate compounds, inorganic) |
| USA ACGIH | ACGIH chemical category | Not Classifiable as a Human Carcinogen |
| USA NIOSH | NIOSH REL (TWA) (mg/m³) | 5 mg/m³ |

8.2.       Exposure Controls

| Appropriate Engineering Controls | : | Emergency eye wash fountains and safety showers should be available in the immediate vicinity of any potential exposure. Ensure adequate ventilation, especially in confined areas. Ensure all national/local regulations are observed. |
| --- | --- | --- |
| Personal Protective Equipment | : | Gloves. Protective clothing. Protective goggles. Insufficient ventilation: wear respiratory protection. |
| Materials for Protective Clothing | : | Chemically resistant materials and fabrics. |
| Hand Protection | : | Wear protective gloves. |
| Eye and Face Protection | : | Chemical safety goggles. |
| Skin and Body Protection | : | Wear suitable protective clothing. |
| Respiratory Protection | : | If exposure limits are exceeded or irritation is experienced, approved respiratory protection should be worn. In case of inadequate ventilation, oxygen deficient atmosphere, or where exposure levels are not known wear approved respiratory protection. |
| Other Information | : | When using, do not eat, drink or smoke. |

# SECTION 9: PHYSICAL AND CHEMICAL PROPERTIES

# 9.1.       Information on Basic Physical and Chemical Properties

| Physical State | : | Solid |
| --- | --- | --- |
| Appearance | : | White crystals or powder |
| Odor | : | Odorless |
| Odor Threshold | : | No data available |
| pH | : | No data available |
| Evaporation Rate | : | No data available |
| Melting Point | : | 75 °C (167 °F) |
| Freezing Point | : | No data available |
| Boiling Point | : | No data available |
| Flash Point | : | No data available |
| Auto-ignition Temperature | : | No data available |
| Decomposition Temperature | : | No data available |
| Flammability (solid, gas) | : | No data available |
| Vapor Pressure | : | No data available |
| Relative Vapor Density at 20°C | : | No data available |
| Relative Density | : | No data available |
| Specific Gravity | : | 1.73 g/ml |
| Solubility | : | Water: Soluble Organic solvent: Glycerol: Soluble Alcohol: Insoluble |
| Partition Coefficient: N-Octanol/Water | : | No data available |
| Viscosity | : | No data available |

9.2.       Other Information  No additional information available

# SECTION 10: STABILITY AND REACTIVITY

10.1.       Reactivity:    Hazardous reactions will not occur under normal conditions.

10.2.       Chemical Stability:    Stable under recommended handling and storage conditions (see section 7).

10.3.       Possibility of Hazardous Reactions:    Hazardous polymerization will not occur.

10.4.       Conditions to Avoid:    Direct sunlight, extremely high or low temperatures, and incompatible materials.

10.5.       Incompatible Materials:    Strong acids, strong bases, strong oxidizers.

10.6.       Hazardous Decomposition Products:    None expected under normal conditions of use.

# SECTION 11: TOXICOLOGICAL INFORMATION

# 11.1.       Information on Toxicological Effects

Acute Toxicity (Oral): Not classified

Acute Toxicity (Dermal): Not classified

Acute Toxicity (Inhalation): Not classified

| Borax (B4Na2O7.10H2O) (1303-96-4) |
| --- |
| LD50 Oral Rat | 3493 mg/kg |
| LD50 Dermal Rabbit | > 10000 mg/kg |
| LC50 Inhalation Rat | > 2 mg/m³ (Exposure time: 4 h) |

Skin Corrosion/Irritation: Not classified

Serious Eye Damage/Irritation: Causes serious eye irritation.

Respiratory or Skin Sensitization: Not classified

Germ Cell Mutagenicity: Not classified

Carcinogenicity: Not classified

Reproductive Toxicity: May damage fertility or the unborn child.

Specific Target Organ Toxicity (Single Exposure): Not classified

Specific Target Organ Toxicity (Repeated Exposure): Not classified

Aspiration Hazard: Not classified

Symptoms/Injuries After Inhalation: Prolonged exposure may cause irritation.

Symptoms/Injuries After Skin Contact: Prolonged exposure may cause skin irritation.

Symptoms/Injuries After Eye Contact: Contact causes severe irritation with redness and swelling of the conjunctiva.

Symptoms/Injuries After Ingestion: Ingestion may cause adverse effects.

Chronic Symptoms: May damage fertility or the unborn child.

# SECTION 12: ECOLOGICAL INFORMATION

# 12.1.       Toxicity

| Ecology - General | : | Harmful to aquatic life. |
| --- | --- | --- |

# 12.2.       Persistence and Degradability

| Sodium Borate (1303-96-4) |
| --- |
| Persistence and Degradability | Not established. |

# 12.3.       Bioaccumulative Potential

| Sodium Borate (1303-96-4) |
| --- |
| Bioaccumulative Potential | Not established. |

# 12.4.       Mobility in Soil  No additional information available

12.5.       Other Adverse Effects

| Other Information | : | Avoid release to the environment. |
| --- | --- | --- |

# SECTION 13: DISPOSAL CONSIDERATIONS

# 13.1.       Waste Treatment Methods

Waste Disposal Recommendations: Dispose of contents/container in accordance with local, regional, national, and international regulations.

Additional Information: Container may remain hazardous when empty. Continue to observe all precautions.

Ecology - Waste Materials: Avoid release to the environment. This material is hazardous to the aquatic environment. Keep out of sewers and waterways.

# SECTION 14: TRANSPORT INFORMATION

The shipping description(s) stated herein were prepared in accordance with certain assumptions at the time the SDS was authored, and can vary based on a number of variables that may or may not have been known at the time the SDS was issued.

14.1.       In Accordance with DOT       Not regulated for transport

14.2.       In Accordance with IMDG    Not regulated for transport

14.3.       In Accordance with IATA      Not regulated for transport

SECTION 15: REGULATORY INFORMATION

# 15.1.       US Federal Regulations

| Sodium Borate (1303-96-4) |
| --- |
| SARA Section 311/312 Hazard Classes | Health hazard - Serious eye damage or eye irritation Health hazard - Reproductive toxicity |

Borax (B4Na2O7.10H2O) (1303-96-4)

Listed on the United States TSCA (Toxic Substances Control Act) inventory

# 15.2.       US State Regulations

Borax (B4Na2O7.10H2O) (1303-96-4)

U.S. - Massachusetts - Right To Know List U.S. - Pennsylvania - RTK (Right to Know) List

SECTION 16: OTHER INFORMATION, INCLUDING DATE OF PREPARATION OR LAST REVISION

| Date of Preparation or Latest Revision | : | 09/30/2019 |
| --- | --- | --- |
| Other Information | : | This document has been prepared in accordance with the SDS requirements of the OSHA Hazard Communication Standard 29 CFR 1910.1200 |

| GHS Full Text Phrases: |
| --- |
| ------ | Aquatic Acute 3 | Hazardous to the aquatic environment - Acute Hazard Category 3 |
| ------ | Eye Irrit. 2 | Serious eye damage/eye irritation Category 2 |
| ------ | Eye Irrit. 2A | Serious eye damage/eye irritation Category 2A |
| ------ | Repr. 1B | Reproductive toxicity Category 1B |
| ------ | H319 | Causes serious eye irritation |
| ------ | H360 | May damage fertility or the unborn child |
| ------ | H402 | Harmful to aquatic life |

This information is based on our current knowledge and is intended to describe the product for the purposes of health, safety and environmental requirements only. It should not therefore be construed as guaranteeing any specific property of the product.

SDS US (GHS HazCom)

False